## Slide 1: Lesson 6 Objectives
Beginning Chapter 2: Energy
Derivation of Multigroup Energy treatment
Finding approximate spectra to make multigroup cross sections
  Assumed (Fission-1/E-Maxwellian)
  Calculated
    Resonance treatments
    Fine-group to Multi-group collapse
Spatial collapse

## Slide 2: Energy treatment
Beginning the actual solution of the B.E. with the ENERGY variable.
The idea is to convert the continuous dimensions to discretized form.
  Infinitely dense variables => Few hundred variables
  Calculus => Algebra
Steps we will follow:
  Derivation of multigroup form
  Reduction of group coupling to outer iteration in matrix form
  Analysis of one-group equation as Neumann iteration
  Typical acceleration strategies for iterative solution

## Slide 3: Definition of Multigroup
All of the deterministic methods (and many Monte Carlo) represent energy variable using multigroup formalism
Basic idea is that the energy variable is divided into contiguous regions (called groups):
Note that it is traditional to number groups from high energy to low.
E0
E1
E2
E3
E4
E5
E6
E7
Group 1
Group 7
Energy

## Slide 4: Multigroup flux definition
We first define the group flux as the integral of the flux over the domain of a single group, g:
Then we assume (hopefully from a physical basis) a flux shape, ,within the group, where this shape is normalized to integrate to 1 over the group.
The result is equivalent to the separation:

## Slide 5: Multigroup constants
We insert this into the continuous energy B.E. and integrate over the energy group: (Why?)
where we have used:

## Slide 6: Multigroup constants (2)
Pulling the fluxes out of the integrals gives:
where

## Slide 7: Multigroup constants (3)
This simplifies to:
if we define:

## Slide 8: Multigroup constants (4)

## Slide 9: Multigroup constants (5)
For Legendre scattering treatment, the group Legendre cross sections formally found by:
From Lec. 4:

## Slide 10: Important points to make
The assumed shapes fg(E) take the mathematical role of weight functions in formation of group cross sections
We do not have to predict a spectral shape fg(E) that is good for ALL energies, but just accurate over the limited range of each group.
  Therefore, as groups get smaller, the selection of an accurate fg(E) gets less and important

## Slide 11: Finding the group spectra
There are two common ways to find the fg(E) for neutrons:
  Assuming a shape: Use general physical understanding to deduce the expected SCALAR flux spectral shapes [fission, 1/E, Maxwellian]
  Calculating a shape: Use a simplified problem that can be approximately solved to get a shape [resonance processing techniques, finegroup to multigroup]

## Slide 12: Assumed group spectra
From infinite homogeneous medium equation with single fission neutron source:
we get three (very roughly defined) generic energy ranges:
  Fission
  Slowing-down
  Thermal

## Slide 13: Fast energy range (>~2 MeV)
Fission source. No appreciable down-scattering:
Since cross sections tend to be fairly constant at high energies:

## Slide 14: Intermediate range (~1 eV to ~2 MeV)
No fission. Primary source is elastic down-scatter:
Assuming constant cross sections and little absorption:
(I love to make you prove this on a test!)

## Slide 15: Thermal range (<~1 eV)
If a fixed number of neutrons are in a pure-scattering equilibrium with the atoms of the material, the result is a Maxwellian distribution:
In our situation, however, we have a dynamic equilibrium:
  Neutrons are continuously arriving from higher energies by slowing down; and
  An equal number of neutrons are being absorbed in 1/v absorption
As a result, the spectrum is slightly hardened (i.e., higher at higher energies) which is often approximated as a Maxwellian at a slightly higher temperature ergies (“neutron temperature”)

## Slide 16: Resonance treatments
Mostly narrow absorption bands in the intermediate range:
Assuming constant microscopic scatter and that flux is 1/E above the resonance (narrow resonance approx):

## Slide 17: Resonance treatments (2)
Reactor analysis methods have greatly extended resonance treatments:
  Extension to other energy scattering situations (Wide Resonance and Equivalence methods)
  Extension of energy methods to include simple spatial relationships
  Statistical methods that can deal with unresolved resonance region (where resonance cannot be resolved experimentally although we know they are there)

## Slide 18: Finegroup to multigroup
“Bootstrap” technique whereby
  Assumed spectrum shapes are used to form finegroup cross sections (G>~200)
  Simplified-geometry calculations are done with these large datasets.
  The resulting finegroup spectra are used to collapse fine-group XSs to multigroup:
E20
E21
E22
E23
E24
E25
E26
E27
Energy
Fine-group structure
E2
E3
Multi-group structure (Group 3)

## Slide 19: Finegroup to multigroup (2)
Energy collapsing equation:
  Using the calculated finegroup fluxes, we conserve reaction rates to get new cross sections
  Assumes multigroup flux will be:
  The resulting multigroup versions are shown on the next page. (I will leave the Legendre scattering coefficients for another day.)

## Slide 20: Finegroup to multigroup (3)

## Slide 21: Related idea: Spatial collapse
We often “smear” heterogeneous regions into a homogeneous region:
Volume AND flux weighted, conserving reaction rate
V1
V2
V=V1+V2

## Slide 22: Homework 6-1
For a total cross section given by the equation:
find the total group cross section for a group that spans from 2 keV to 3 keV. Assume flux is 1/E.

## Slide 23: Homework 6-2
Find the isotropic elastic scatter cross section for Carbon-12 (A=12) from an energy group that spans from 0.6 to 0.7 keV to a group that spans 0.4 keV to 0.5 keV. Assume the flux spectrum is 1/E and that the scattering cross section is a constant 5 barns.
[Hint: The distribution of post-collision energies for this case is uniform from the pre-collision neutron energy down to the minimum possible post-collision energy of aE.]

## Slide 24: Homework 6-3
For the same physical situation as in the previous problem, find the within-group scattering cross sections for the energy group that spans from 0.6 to 0.7 keV.